## Slide 1: Maze navigation based on auditory cues
Cathy Oun
Jeffery alcock
June 2nd 2015

## Slide 2: Motivation
Virtual Reality
  “An artificial world that consists of images and sounds created by a computer and that is affected by the actions of a person who is experiencing it.” – Merriam-Webster Dictionary
Replace reliance on visual feedback with audio feedback to indicate direction
Entertainment

## Slide 3: Surround Sound
Surround sound gives a sense of direction to an observer listening to an audio source
Can be achieved with stereo hardware (i.e. ear buds) by a compilation of basic filtering effects
  Delay
  Volume Manipulation
  Frequency Filtering

## Slide 4: Surround Sound Technical Details
We chose to quantize the granularity of the surround sound to 8 different regions surrounding the user
Delay:
  The distance from a source to each ear can vary by direction based on simple geometry.

## Slide 5: Surround Sound Technical Details (2)
Volume Manipulation:
  Sound Shadow – refers to the absorption of sound by an object in its path.
  Interaural Intensity Difference – describes the differences in the sound perceived by both ears. These differences allow the human brain to localize sound and determine origin information.
  tl;dr make the far ear quieter
[1]

## Slide 6: Surround Sound Technical Details (3)
Frequency Filtering:
  Human ears are oriented in order to hear in front of them. The outer structure of the ear (the Pinna) allows sound to bounce off in various ways to orient the listener.
  We chose to model this as an exaggerated head shadow effect. When a sound source is behind the listener, we low pass filter the sound to emulate the loss of information caused by the Pinna.
[1]

## Slide 7: Application: A Maze Solving Game!
Move Counter
User Position/Direction
Hidden Sound Source
User Feedback Message
Play Again Button
Path
Wall

## Slide 8: Maze User Controls
Game Objective: Navigate to the hidden sound source using the auditory cues presented.
  Ear buds are used to observe various audio signals
    Static ambient jungle noise
    Dynamic trumpet fanfare (emitted from the destination)
  Keyboard used to move the user
    Four arrow keys move the user along the maze path
    W, A, S, D change the direction the user is facing
      W = face up, A = face left, S = face down, D = face right
Finishing the Game: A celebratory sound is played, a win message is displayed, and the Play Again button is enabled to reset the game.

## Slide 9: Block Diagram
Ear buds
Bundled
sound
parameters
Audio Processing
Delay
Intensity manipulation
filtering
Back-End
Data Management
Sound Playing
GUI Creation Update
User keyboard input

## Slide 10: MATLAB Code
Back-end: data management
  currentRow, currentCol
  destinationRow, destinationCol
  distance, direction, lowPassIndex
  Open SerialChannel to send data to C
Music: import and play sounds
  Load sound files, create audioplayer object to loop sound
  Play sounds through separate channels so C can process them individually
GUI: display maze and user feedback
  Custom GUI (figure, uipanel, cell array of axes)

## Slide 11: MATLAB Flow Diagram
mazeMain
creatGUI
key_pressed_fcn
updateSoundModule
updateGUI
initializeGUI
reset_maze_fcn
if(gameOver)
Send to C
uart

## Slide 12: Sending Data from MATLAB to C
The following parameters are packaged together as a string and sent via UART to Eclipse
  distance
    0 – 9, 0 representing very close to the sound source, and 9 representing very far away from the sound source
  lowPassIndex
    0 – 9, representing various degrees of filtering
    0-2, 3-5, 6-9 are all processed as different low pass filters with an increasingly small cutoff for more extreme low pass filtering
  direction
    0 – 7, representing the 8 possible directions of the sound source

## Slide 13: Algorithms
Distance & Intensity: Pythagorean theorem
  Sqrt((destX-currX)^2 + (destY-currY)^2)
  Inverse-square law: 1/(distance^2)
Low Pass Index:
  Currently modeled the same as
  distance
  Future work should incorporate
  shortest path
Direction: 8 different regions
  Calculate the slopes of each region
  Set the boundaries (in our case, between 0.25 and 4)
[4]

## Slide 14: C Code
Receives bundled parameters from MATLAB using the UART connection
  uart_byte_recv(void)
Stores the characters in the rx_buffer
Every time new data is received, the buffer is sent to the sound_module(distance, lowPassIndex, direction)
The sound_module changes the leftChannelData, rightChannelData by applying delay, intensity manipulation, and frequency filtering

## Slide 15: References
[1] Brian Shannan, “Audiology-A Curriculum for Excellence”, 25 Nov 2010. Web. 30 May 2015. http://www.ssc.education.ed.ac.uk/courses/deaf/dnov10i.html
[2] Youtube Audio Library. Web. 30 May 2015. https://www.youtube.com/audiolibrary/music
[3] MathWorks-Instrument Control Toolbox. Web. 30 May 2015. http://www.mathworks.com/products/instrument/supported/serial.html [4] Pythagorean theorem. Web. 30 May 2015.
http://en.wikipedia.org/wiki/Pythagorean_theorem
[5] Inverse-square Law, Wikipedia. Web. 30 May 2015 http://en.wikipedia.org/wiki/Inverse-square_law
[6] Conor O’Sullivan “A Formulation of Holophonic Display”, 5 July 2012. Web. 30 May 2015. https://www.academia.edu/2931477/A_Formulation_of_Holophonic_Display

## Slide 16: Thank you